## Slide 1: Using the FLDPLN Model for Flood Inundation Model
Introduction to the FLDPLN FIM model
Use Wildcat Creek, KS Labor Day flood event as an example
Workshop materials
  Notebooks, Python packages and tools are on GitHub
    https://github.com/XingongLi/fldpln
    fldpln_py, MATLAB Runtime installer (without MATLAB Runtime), fldpln and ArcGIS toolbox
  Wildcat Creek data is on KU KBS-KARS server
    DEMs, segment shapefiles, gauge data and reference FIM map
  Installer with MATLAB Runtime included on KU KBS-KARS server
About 6 hours

## Slide 2: Low Complexity FIM Models
Hydrodynamic models are more accurate but need more data and computational resources
Low complexity models are faster and need few inputs
  Faster at high resolution over large areas
  Hydro-conditioned DEM as the primary input
Especially useful in predicting inundation extent and depth that are likely to occur in the immediate future using observed or forecasted stream stage

## Slide 3
Low-complexity flood inundation model based on backfill and spillover flooding mechanisms
Q
P
}
d
water surface
ground surface
downhill flow
(overland flow)
flow
Spillover
Flooding
“Water flows downhill”
“Water seeks its own level”
uphill flow
(swelling)
Q
P
d
water surface
ground surface
flow
Backfill
Flooding
The FLDPLN (floodplain) Model

## Slide 4: Major Processes
FLDPLN
Hydro-conditioning DEM
FLDPLN inundation modeling
Segment to tiled libraries
Inundation mapping

## Slide 5: Hydro-Condition DEM
Processing of a DEM so that the flow of water is continuous across the terrain surface
Tools
  GIS (ArcHydro) and special tools
Examples
  Fill spurious sinks or pits
  Add breach lines to drain sinks
    Burning culverts into roads
    Cut through bridges above river
    Burning spillway into dam
  Add flood defense (levees and flood walls) into DEM
  Mask out large waterbodies

## Slide 6
Segment-based modeling with FLDPLN
upstream
segment
spillover taper
(depth decay)
downstream
segment
backfill taper
(lake effect)
flow
flow

## Slide 7: Flood Inundation Relations
A floodplain pixel (FPP) can be flooded by the water originated from flood source (stream) pixels (FSPs) through backfill and spillover flooding
  FSP-FPP flood relation
  many-to-many relation
Depth to flood (DTF)
  Minimum depth at a FSP needed to flood a FPP
  Attribute associated with a FSP-FPP relation
FLDPLN model identifies the FSP-FPP flooding relations and their associated DTFs
  Iterative process
5
3
1
(FSP)
(FPP)
(DTF)

## Slide 8: Tile FSP-FPP Inundation Relations
Organize relations by tiles
  Each tile stores all the FSPs that can flood the FPPs in the tile
Flood mapping by tiles
  Avoid memory overflow with a proper tile size
  Only one file I/O is needed to map a tile
  Scalable
    Mapping tiles in parallel
    Each tile can be mapped independently

## Slide 9: Flood Inundation Mapping
Estimate FSP depth of flow (DOF) from gauge observation or forecast
  Snap gauges to FSPs
  Based on steam orders
    From low to high
  Linear interpolation using
  distance or elevation
Stage sources
  NWS AHPS and USGS
  NWM + HAND SRC

## Slide 10: Inundation Mapping
Interpolated FSP DOF
A FPP is flooded by a FSP if its DOF > DTF
  FloodDepthFSP(i) = DOFFSP(i) - DTFFSP(i)
Flood depth at a FPP
  max(FloodDepthFSP(1), …, FloodDepthFSP(n))
  N is the number of FSPs that flood the FPP
Example
  Flood depth = max((5-3), (7-1)) = 6
5
3
1
5
7
3

## Slide 11: Parallel Inundation Mapping
Time sensitive application
Tiled libraries ready for parallelization
Dask with custom directed acyclic graph (DAG)

## Slide 12
Mapping Sep. 3, 2018 Wildcat Creek Flood

## Slide 13
HAND and FLDPLN FIM with 10-m DEM

## Slide 14: Mapping Wildcat Creek 2018 Labor Day Flood
Data in wildcat_10m_3dep.zip
  DEM (GeoTIFF and BIL)
  Event gauge data
  Reference inundation map
  Segment shapefiles
MATLAB Runtime and Python packages are only for Windows

## Slide 15: Mapping Wildcat Creek 2018 Labor Day Flood
Hydro-condition DEM
  No conditioning for the DEM
Convert hydro-conditioned DEM (in GeoTIFF) into BILs
  ArcGIS toolbox fldpln preprocess model.atbx
  fldpln_pre_process_tool tool

## Slide 16: Mapping Wildcat Creek 2018 Labor Day Flood
Build a Python environment for FLDPLN
  00_build_fldpln_python_env.md
  Install miniconda
  Install mamba in the base env
    conda install -c conda-forge mamba
  Create the fldpln environment using fldpln_windows.yaml
    mamba env create -f fldpln_windows.yaml
  Activate the fldpln environment
    conda activate fldpln
  Install additional packages for using the environment in JupyterLab or VSC
    mamba install -c conda-forge jupyterlab
mamba env create -f fldpln.yaml

## Slide 17: Mapping Wildcat Creek 2018 Labor Day Flood
Build a Python environment for FLDPLN
  In the command window, navigate to the training folder and start JupyterLab from there
    jupyter lab
  Install fldpln_py
    Run one of the two Windows installer
    Locate where the fldpln_py is installed and activate fldpln env
    Navigate to fldpln_py folder which has setup.py and use:
      python setup.py install
      pip install .
  Install fldpln package
    pip install fldpln
mamba env create -f fldpln.yaml

## Slide 18: Mapping Wildcat Creek 2018 Labor Day Flood
Build segment-based library
  01_build_segment_library.ipynb
  Identify stream networks and generate segments (2 miles typically)
  Select segments (16) for Wildcat Creek
Tile segment-based library
  02_build_tiled_library.ipynb
  For fast parallel mapping
  Assign stream order for stage interpolation

## Slide 19: Mapping Wildcat Creek 2018 Labor Day Flood
Create special maps
  03_mapping_special.ipynb
  Minimum DTF, # of FSPs, constant stage
Map inundation for flood events
  04_mapping_event.ipynb
  2018 Labor Day event
    USGS/AHPS gauge stage
    NWM + HAND SRC stage
Mapping by segment (for building new rating curve)
  05_mapping_segment.ipynb

## Slide 20
Old Libraries (25) with 5-m DEM

## Slide 22: New Libraries (8) with New 5-m DEM

## Slide 23: Changing Libraries and Code
Model is currently run for 8 libraries
  Segment-based libraries are almost done
Code
  MATLAB
  Python
  Both code has been changed for new libraries

## Slide 24: Future Plan
FLDPLN model component
  Support both Windows & Unix
    YAML file for each OS
    fldpln_py for each OS
  Python class wrapper for fldpln_py
    Hide data conversion from user
  Make it available and installable from GitHub
  Turn it into PyPI package
  Re-implement it in Python?
FLDPLN mapping component
  docstrings for the functions
  Automatic stream order assignment
  Turn it into a PyPI package

## Slide 25: Acknowledgements
Jude and graduate students @KU
James and Junho @UA
Funding
  GIS-PB
  Kansas Water Office (KWO) / KDEM

## Slide 26: Questions?
Xingong Li
lixi@ku.edu