## Slide 1: Using the FLDPLN Model for Flood Inundation Mapping
Introduction to the FLDPLN FIM model
Use Wildcat Creek, KS Labor Day flood event as an example
Workshop materials
  Notebooks, Python packages and tools are on GitHub
    https://github.com/XingongLi/fldpln
    fldpln_py, MATLAB Runtime installer (without MATLAB Runtime), fldpln and ArcGIS toolbox
  Wildcat Creek data is on KU KBS-KARS server
    DEMs, segment shapefiles, gauge data and reference FIM map
  Installer with MATLAB Runtime included is on KU KBS-KARS server
About 6 hours

## Slide 2: Low Complexity FIM Models
Hydrodynamic models are more accurate but need more data and computational resources
Low complexity models are faster and need few inputs
  Faster at high resolution over large areas
  Hydro-conditioned DEM as the primary input
Especially useful in predicting inundation extent and depth that are likely to occur in the immediate future using observed or forecasted stream stage

## Slide 3
Low-complexity flood inundation model based on backfill and spillover flooding mechanisms
Q
P
}
d
water surface
ground surface
downhill flow
(overland flow)
flow
Spillover
Flooding
“Water flows downhill”
“Water seeks its own level”
uphill flow
(swelling)
Q
P
d
water surface
ground surface
flow
Backfill
Flooding
The FLDPLN (floodplain) Model

## Slide 4: Major Processes
FLDPLN
Hydro-conditioning DEM
FLDPLN inundation modeling
Segment to tiled libraries
Inundation mapping

## Slide 5: Hydro-Condition DEM
Processing of a DEM so that the flow of water is continuous across the terrain surface
Tools
  GIS (ArcHydro) and special tools
Examples
  Fill spurious sinks or pits
  Add breach lines to drain sinks
    Burning culverts into roads
    Cut through bridges above river
    Burning spillway into dam
  Add flood defense (levees and flood walls) into DEM
  Mask out large waterbodies

## Slide 6
Segment-Based Modeling with FLDPLN
upstream
segment
spillover taper
(depth decay)
downstream
segment
backfill taper
(lake effect)
flow
flow

## Slide 7: Flood Inundation Relations
A floodplain pixel (FPP) can be flooded by the water originated from flood source (stream) pixels (FSPs) through backfill and spillover flooding
  FSP-FPP flood relation
  many-to-many relation
Depth to flood (DTF)
  Minimum depth at a FSP needed to flood a FPP
  Attribute associated with a FSP-FPP relation
FLDPLN model identifies the FSP-FPP flooding relations and their associated DTFs
  Iterative process
5
3
1
(FSP)
(FPP)
(DTF)

## Slide 8: Tile FSP-FPP Inundation Relations
Organize relations by tiles
  Each tile stores all the FSPs that can flood the FPPs in the tile
Flood mapping by tiles
  Avoid memory overflow with a proper tile size
  Only one file I/O is needed to map a tile
  Scalable
    Mapping tiles in parallel
    Each tile can be mapped independently

## Slide 9: Flood Inundation Mapping
Estimate FSP depth of flow (DOF) from gauge observation or forecast
  Snap gauges to FSPs
  Based on steam orders
    From low to high
  Linear interpolation using
  distance or elevation
Stage sources
  NWS AHPS and USGS
  NWM + HAND SRC

## Slide 10: Inundation Mapping
Interpolated FSP DOF
A FPP is flooded by a FSP if its DOF > DTF
  FloodDepthFSP(i) = DOFFSP(i) - DTFFSP(i)
Flood depth at a FPP
  max(FloodDepthFSP(1), …, FloodDepthFSP(n))
  N is the number of FSPs that flood the FPP
Example
  Flood depth = max((5-3), (7-1)) = 6
5
3
1
5
7
3

## Slide 11: Parallel Inundation Mapping
Time sensitive application
Tiled libraries ready for parallelization
Dask with custom directed acyclic graph (DAG)

## Slide 12
Mapping Sep. 3, 2018 Wildcat Creek Flood

## Slide 13
HAND and FLDPLN FIM with 10-m DEM

## Slide 14: Mapping Wildcat Creek 2018 Labor Day Flood
Wildcat Creek data is on KU KBS-KARS server
  DEM (GeoTIFF and BIL)
  Gauge data
  Reference inundation map
  Segment shapefiles (not necessary but just in case)
Notebooks, Python packages and tools are on GitHub
Installer with MATLAB Runtime included is on KU KBS-KARS server

## Slide 15: Prepare DEM
Hydro-condition DEM
  No conditioning for the Wildcat DEM
Convert hydro-conditioned DEM (in GeoTIFF) into BILs
  ArcGIS toolbox fldpln preprocess model.atbx
  fldpln_pre_process_tool tool

## Slide 16: Build the fldpln Python environment
00_build_fldpln_python_env.md
Major steps
  Install miniconda and mamba
  Create the fldpln environment using fldpln_windows.yaml
  Install MATLAB runtime and the fldpln_py package
  Install fldpln package
  Install JupyterLab or VSC if necessary

## Slide 17: Build segment-based Library
01_build_segment_library.ipynb
Major steps
  Identify stream networks and generate segments
  Select segments and prepare spatial mask
  Create raw segment-based library
  Reformat segment-based library
  Generate stream order

## Slide 18: Tile segment-based Library
02_build_tiled_library.ipynb
Major steps
  Tile segment-based library
  Calculate FSP and segment downstream distance
  Assign stream order to FSPs and segments

## Slide 19: Create Special Maps
03_mapping_special.ipynb
Four special maps
  Minimum depth to flood map
  Number of FSP map
  Depression depth map
  Constant FSP stage map (all the FSP has the same stage)

## Slide 20: Map Flood Events
04_mapping_event.ipynb
Major steps
  Prepare gauge stage elevation
  Snap gauge to FSPs
  Interpolate FSP stage
  Create inundation depth map

## Slide 21: Acknowledgements
Jude and graduate students @KU
James and Junho @UA
Funding
  GIS-PB
  Kansas Water Office (KWO) / KDEM
Contact
  Xingong Li (lixi@ku.edu)